PT01 PIR Thermostat (230V)

A.	Installation, Mounting:

Caution:	Turn off PT01 and any electrical devices connected (e.g. heater) before installation.

It is highly recommended that the installation procedure is processed by trained personnel.

1.	Installation Location:

The PIR thermostat should be mounted no higher than 2.4m above the floor inside the room and in a position where it is readily affected by changes of the general room temperature with freely circulating air. It is important to Prevent direct exposure to sunlight; or wet areas. Do not place in a location where the thermostat could be affected by draughts or open windows etc. Do not place the thermostat near direct heat/cool generating sources.

2. Wiring:

Caution: Turn off the electrical devices before wiring.

There are 2 groups of wiring terminals(N, L and L1, L2) at the bottom of PT01. Connect heater to the "L1” and "L2" terminals and connect 230Vac to “L” and “N”. Wire the correct cables to the terminal block according to the circuit diagram which is attached inside the thermostat top cover.

Push all cables back into wall prior to fixing to avoid trapping wires.

3.	Mounting:

Using the accessory screws and wall anchors provided, mount PT01 with the key-hole at the back.

- Temperature and Comfort Mode Delay Time Setting.

Caution: Disconnect the electrical devices and Power of PT01 before Setting.

Open the Cover of PT01 and you will see there are two Circuit Boards

Comfort Mode Delay Time Setting.

There are three Jumpers in the top circuit board. It is possible to select the Comfort mode delay time by accessing the Jumper S1 in the left hand side. (Please Keep Jumper S2 and S3 placed in the “Use” Position)

When the 2Hrs option is selected, the Comfort Mode Delay Time will be 2 Hours. When the 1Hr option is selected, the Comfort Mode Delay Time will be 1 Hour

*PT01 will go to Comfort Mode for 1 hour or 2 hours first (depends on the jumper selection) when the power is turned on.

Temperature Setting.

You can set  Both Comfort mode Temperature and Economy mode Temperature by turning the potentiometers in the Bottom Circuit Board.

To set the economy mode temperature, turn the potentiometer in the left from 5 to 16 ºC.

To set the comfort mode temperature, turn the potentiometer in the right from 16 to 30 ºC.

- Specification:

Supply Voltage:	230Vac 50/60Hz

Load Voltage:	24…240Vac (potential free)

Load Current:	16A max.

Terminal block connecting Label: